## Slide 1: CPTR 380 Hardware Design
Custom CPU with 8-bit architecture

## Slide 2: Overview
Project Tasks
  Created a custom-designed instruction set
  Create assembler
  Design a CPU to execute instruction set
  Implement this hardware by describing it in C++
Aimed at a histogram equalization routine of a simple greyscale image with up to 256 shades

## Slide 3: Workflow
Brainstorming Possible Ideas
Design Process
Testing
Rinse, Repeat
Assembler
Hardware Implementation
CPU
Instruction Set
Testing

## Slide 4: Instruction specs
Instructions will be 16 bits wide
16 OP codes (4 bits each)
16 8-bit registers
256 bytes of memory
No direct operations on memory (LW then ADD, not same step)
Only loading from memory (LM, use an ADD for registers and immediate)

## Slide 5: Instruction Format
Type | Opcode | DestReg | SrcReg1 | SrcReg2
R | 4 bits | 4 bits | 4 bits | 4 bits
Type | Opcode | Regw/address | Unused
B | 4 bits | 4 bits | 8 bits
Type | Opcode | Register | Address
I | 4 bits | 4 bits | 8 bits

## Slide 6: Instruction Library
Type | Opcode | Format | Address
Load |  |  | 
 | LM | LM R1, 0x45 | 0x2
Store |  |  | 
 | ST | ST R1, 0x45 | 0x3
Branch |  |  | 
 | BEQ | BEQ R1, R2, R3 | 0x6
 | BGT | BGT R1, R2, R3 | 0x7
 | BLT | BLT R1, R2, R3 | 0x8
 | B | B R3 | 0x9

## Slide 7: Instruction Library
Type | Opcode | Format | Address
Add |  |  | 
 | ADDI | ADDI R1, R2, 5 | 0xA
 | ADD | ADD R2, R2, R3 | 0xB
Subtract |  |  | 
 | SUBI | SUBI R1, R2, 5 | 0xC
 | SUB | SUB R1, R2, R3 | 0xD
Shift |  |  | 
 | SL | SL R1, R2, 10 | 0xE
 | SR | SR R1, R2, 10 | 0xF

## Slide 8: Instruction Library
Type | Opcode | Format | Address
Logic |  |  | 
 | AND | AND R1, R2, R3 | 0x0
 | OR | OR R1, R2, R3 | 0x1
End |  |  | 
 | END | END | 0x4

## Slide 9: Assembler (import txt)
file = "assemblerInput.txt"
filehandle = open("assemblerInput.txt","r")
with filehandle:
for line in filehandle:
tokenized_line = line.split()

## Slide 10: Assembler (instruction to binary)
if tokenized_line[0] =="LM":
r=int(tokenized_line[1][1])
hex = tokenized_line[2]
hex_list = hex.split("x")
v=int(hex_list[(1)])
b=[2,r,v>>4,v&0xF]
i=bin(b[0])
j=bin(b[1])
k=bin(b[2])
l=bin(b[3])
m=[i,j,k,l,]

## Slide 11: Assembler (output to txt)
lines = m
with open('assemblerOutput.txt', 'w') as f:
for line in lines:
f.write(line)
f.write(' ')
f.write('\n')

## Slide 12: Hardware Design

## Slide 13: Overview

## Slide 14: ALU Schematic

## Slide 15: Software Simulation
C++
Each block (in general) is relegated to a function

## Slide 16: Accumulating Program Memory
Read assembler output (fstream)
Copy into a temp array (sstream)
Convert to ulong
Read into program memory

## Slide 17: ALU
4 different options for arithmetic
Also has compare functionality
Control Line Selection bus
Also triggers branch flag for beq, blt, and bgt instructions

## Slide 18: Bits and Pieces
Program Memory
Main Memory
Control Unit
Program Counter
Registers

## Slide 19: Questions? (demonstration time permitting)

## Slide 20: Thank You